## Slide 1: Methodology: Collagen Fibril Orientation Analysis
Image Processing & Quantitative Comparative Analysis
Based on Polarized Light Microscopy (PLM)

## Slide 2: Workflow Algorithm
1. Image Acquisition & Preprocessing (HSV Conversion)
2. ROI Selection & Noise Masking
3. Standardized Zone Segmentation (SZ, MZ, DZ)
4. Reference-Based Color Calibration
5. Mathematical Angle Calculation
6. Comparative Analysis (Healthy vs. Degraded)

## Slide 3: 1. Image Processing & Masking
• Input: PLM Image (BGR format).
• Conversion: Transformed to HSV Color Space.
- Hue (0-179): Encodes fibril orientation.
- Saturation (S) & Value (V): Used for filtering.
• Noise Reduction: Dual-threshold mask applied.
- Excluded pixels where S < 10 or V < 10.
- Ensures analysis only on birefringent tissue.

## Slide 4: 2. Standardized Zone Segmentation
• Zones defined by normalized tissue thickness:
- Superficial Zone (SZ): 0% – 10%
- Middle Zone (MZ): 10% – 40%
- Deep Zone (DZ): 40% – 100%
• Purpose: Ensures anatomical consistency across all samples (Femoral, Tibial, etc).

## Slide 5: 3. Reference-Based Calibration
• Reference Image: One healthy sample selected per group (e.g., Healthy Femur).
• Anchors Defined:
- H₀: Median Hue of SZ (mapped to 0°).
- H₉₀: Median Hue of DZ (mapped to 90°).
• Application: These H₀ and H₉₀ values are applied to all degraded samples (EOA, MOA, AOA) for direct comparison.

## Slide 6: 4. Angle Calculation Model
• Equation: θ = [(H − H₀) / (H₉₀ − H₀)] × 90°
• Method:
- ROI sliced into 100 normalized depth bins.
- Circular mean hue calculated for each bin.
- Linear interpolation determines angle θ.
• Result: Continuous depth-dependent orientation profile.

## Slide 7: 5. Comparative Analysis Framework
• Groups Analyzed:
- Healthy Reference (Baseline)
- Early OA (EOA)
- Moderate OA (MOA)
- Advanced OA (AOA)
• Metric: Overlay of Depth vs. Angle curves.
• Goal: Quantify loss of surface tangency and structural disorganization.